## Slide 1
01
Residential
Energy System
Optimizer
MILP-Driven Solar & Storage Sizing
43K+
Variables
61K+
Constraints
8,760
Hours Modeled
Dynamic Data Ingestion
Fetches real irradiance via Open-Meteo API. Builds localized 8760-hr load profiles from 5-year EIA data with 9 geographic variability factors. Applies SDG&E TOU tariff schedules.
Real-World Hardware Catalogs
Built-in 2025 equipment catalog (REC, Maxeon, Tesla, Enphase). Auto-selects panels & batteries to maximize efficiency-to-cost ratio ($/Wp or $/kWh).
Physical Roof Geometry
Maps user-defined roof dimensions to exact panel fit. Tests portrait & landscape orientations to maximize utilization while optimizing string wiring for 400V inverter limits.
Joint MILP Optimization
Uses scipy.optimize.milp (HiGHS solver) to simultaneously optimize discrete panel count + continuous battery capacity alongside full 8760-hr dispatch in a single pass.
ECE 285 · UCSD · Residential Solar Optimization

## Slide 2
02
Optimization Engine & Financial Output
MILP Solver · Dual-Scenario A/B Testing · 10-Year NPV Engine
OPTIMIZATION LOGIC
Objective: Minimize Total Cost of Ownership
(Amortized Net CAPEX) + (Grid Import Costs) − (NEM 3.0 Export Credits)
Strict Physical Constraints:
Power Balance
Load = PV + Discharge + Import − Charge − Export (every hour)
Battery Health
10% DoD floor · 50% cap/hr charge limit · 97.5% round-trip efficiency
Capital Limits
Enforces user budget cap and physical roof area constraints
FINANCIAL OUTPUT
A/B Dual-Scenario Comparison:
PV Only
Payback: 1 yr
NPV: $17,791
CAPEX: $507
PV + Battery
Payback: 4 yr
NPV: $9,250
CAPEX: $13,157
10-Year Financial Engine:
30% Federal ITC applied to net CAPEX
6% annual utility inflation rate
7% discount rate for NPV calculation
0.5%/yr panel degradation factor
Year-10 inverter replacement reserve
ECE 285 · UCSD · Residential Solar Optimization

## Slide 3: Optimization tool
Overview: A comprehensive Python-based tool that automates the sizing, physical layout, and dispatch scheduling of residential solar and storage systems using a Mixed-Integer Linear Programming (MILP) engine.
Key Capabilities:
Dynamic Data Ingestion: Automatically fetches historical irradiance (Open-Meteo API), builds localized 8760-hour load profiles (using downscaled 5-year EIA data with 9 geographic/demographic variability factors), and applies real SDG&E Time-of-Use (TOU) tariffs.
Real-World Hardware Catalogs: Features a built-in 2025 equipment catalog (e.g., REC, Maxeon, Tesla, Enphase). The system automatically selects panels and batteries to maximize the efficiency-to-cost ratio ($/Wp or $/kWh).
Physical Roof Geometry ("Tetris" Math): Maps user-defined roof dimensions to calculate exact physical fit. It tests both portrait and landscape orientations to maximize roof area utilization while optimizing electrical string wiring for 400V inverter limits.
Joint 8760-Hour MILP Optimization: Utilizes scipy.optimize.milp (HiGHS solver) to simultaneously optimize capital sizing (discrete panel count, continuous battery capacity) alongside a full 8760-hour dispatch schedule in a single pass—avoiding the flaws of "simulate-after-sizing" heuristics.

## Slide 4: Optimization tool continued
Optimization Logic: The MILP solver evaluates over 43,000 variables and 61,000 constraints to minimize the annualized Total Cost of Ownership.
The Objective Function: Minimizes (Amortized Net CAPEX) + (Grid Import Costs) – (NEM 3.0 Export Credits).
Strict Physical Constraints: * Power Balance: $Load = PV_{gen} + Discharge + Import - Charge - Export$ (enforced every hour).
  Battery Health limits: Enforces a 10% Depth-of-Discharge (DoD) floor, limits charge/discharge to 50% of capacity per hour, and accounts for round-trip efficiency losses ($\eta = 97.5\%$).
  Capital Limits: Ensures the selected hardware respects the user's maximum budget and roof area.
Financial Output & Dual-Scenario Comparison:
A/B Testing: The orchestrator runs the solver twice to directly compare a "PV-Only" architecture against a "PV + Battery" architecture.
10-Year Financial Engine: Computes exact Payback Period and Net Present Value (NPV) by factoring in the 30% Federal ITC, 6% annual utility inflation, 7% discount rate, annual panel degradation ($0.5\%/yr$), and a Year-10 inverter replacement reserve.
Actionable Output: Returns a highly detailed configuration dictionary containing cell-level specs, exact string configurations, required battery units, and a year-by-year cash flow breakdown.

## Slide 5: Optimization tool continued

## Slide 6
Residential Energy
System Optimizer
A Python MILP Framework for Solar + Storage Sizing
A comprehensive Python tool that automates the sizing, physical layout, and dispatch scheduling of residential solar+storage systems using a joint Mixed-Integer Linear Program — solving capital sizing and 8760-hour dispatch in a single pass.
43,803
MILP Variables
8,760
Hours Modeled
2 runs
PV-Only vs PV+Bat
Dynamic Data Ingestion
Roof Geometry ('Tetris')
Joint MILP Optimization
10-Year Financial Engine
ECE 285 · UCSD · Residential Solar Optimization | Slide 1 of 4

## Slide 7
02
System Inputs
User Profile · External APIs · Hardware Catalogs · Tariff Data
USER PROFILE
Location
32.7157°N, 117.1611°W
Budget
$50,000
Roof Dims
3.0 m × 5.0 m (15 m²)
Tariff Plan
TOU_DR (SDG&E)
Annual Load
18,000 kWh/yr
Occupants
1
EIA LOAD PROFILE
Source
EIA 5-yr average
Years
2021 to 2025
Annual Total
18,000 kWh
Avg Power
2.055 kW
Variability Factors
9 geographic / demographic
Customers
1,040,149 SDG&E meters
OPEN-METEO IRRADIANCE API
Annual GHI
1,924.6 kWh/m²/yr
Data Points
8,760 hourly values
Reference Irr.
1,000 W/m² (STC)
Model
Sine daylight shape factor
Coord
32.7157°N, 117.1611°W
Temp Adj.
−0.29%/°C (cell coeff.)
SDG&E TARIFF SCHEDULE
Plans
TOU_DR, TOU-DR1, TOU-DR2
Avg Rate
$0.4951 / kWh
Period
2021–2025 historical CSV
Export Credit
NEM 3.0 (net billing)
Peak Hours
4 PM – 9 PM on-peak
Off-Peak
Super off-peak overnight
PANEL CATALOG (2025 EnergySage)
Model
Eff
$/Wp
Canadian Solar TOPHiKu7
23.2%
$0.16/Wp
Aiko Solar Neostar 2P
24.3%
$0.55/Wp
Maxeon 7
24.1%
$3.50/Wp
Jinko Tiger Neo
22.5%
$0.45/Wp
REC Alpha Pure
21.9%
$0.83/Wp
LONGi Hi-MO 6
22.3%
$0.30/Wp
Silfab Prime
22.6%
$0.53/Wp
★ Selected by optimizer (best efficiency/cost ratio)
BATTERY CATALOG
Model
Cap
RTE
Generac PWRcell M6
18 kWh
96.5%
Tesla Powerwall 3
13.5 kWh
97.5%
Enphase IQ10T
10.1 kWh
96%
Franklin WH10
10 kWh
98%
SolarEdge H10K
9.7 kWh
94.5%
ECE 285 · UCSD · Residential Solar Optimization | Slide 2 of 4

## Slide 8
03
Processing Pipeline
Roof Geometry · Panel Selection · MILP Formulation · HiGHS Solver · Constraints
STEP 1 — ROOF GEOMETRY ("TETRIS")
Roof Input
3.0 m × 5.0 m = 15.0 m² usable area
Orientation Test
Tests BOTH portrait and landscape for every panel model to maximize roof utilization
Panel Footprint
Canadian Solar TOPHiKu7: 3.11 m² per panel (1.722 m × 1.134 m × 2 parallel cells)
Fit Result
Landscape: 2 cols × 2 rows = 4 panels
Utilization: 100.0% (12.44 / 15.0 m²)
String Wiring
4S × 1P strings → 163.2 V DC bus
Optimized toward 400 V inverter target
DC Capacity
4 × 720 W = 2.88 kW DC array
Array current: 17.67 A
STEP 2 — MILP FORMULATION
Variable Layout (5T+3 total)
idx 0: Panels (integer)
idx 1: BatCap kWh (continuous)
idx 2..T+1: Import(t) per hour
idx T+2..2T+1: Export(t)
idx 2T+2..3T+1: Charge(t)
idx 3T+2..4T+1: Discharge(t)
idx 4T+2..5T+2: SOC(t)
Scale (T = 8,760 hours)
Variables: 43,803
Constraints: 61,325
Sparse NNZ: 166,449
Objective Function
Minimize:
(Amortized Net CAPEX)
+ Σ price(t)·Import(t)
− Σ export_credit(t)·Export(t)
STEP 3 — CONSTRAINTS + SOLVER
Power Balance (every hour)
Load(t) = PV(t) + Discharge(t) + Import(t)
− Charge(t) − Export(t)
Battery Health
SOC floor: 10% DoD minimum
Max charge/discharge: 50% cap/hr
Round-trip efficiency: η = 96.5%
SOC continuity: SOC(t+1) = SOC(t)
+ Charge(t)·η − Discharge(t)/η
Capital Limits
Panels ≤ max_panels_fitting_roof (4)
Total CAPEX ≤ user_budget ($50K)
BatCap ≥ 0 (relaxed to continuous)
HiGHS Solver (dual run)
Run 1 — PV Only: 11.58 s → Optimal
Run 2 — PV + Battery: 11.22 s → Optimal
Solver: scipy.optimize.milp (HiGHS)
PV Generation Model
PV(t) = N·P_panel·(G(t)/G_ref)·PR
Perf. Ratio PR = 0.80
Degradation: 0.4%/yr (TOPHiKu7)
ECE 285 · UCSD · Residential Solar Optimization | Slide 3 of 4

## Slide 9
04
Results & Financial Output
Hardware Config · PV-Only vs PV+Battery · 10-Year Cash Flow · NPV / Payback
SELECTED HARDWARE
SOLAR CELL / PANEL
Model
Canadian Solar TOPHiKu7
Cell P_max
5.4545 W
Cell V_mp
0.6182 V | I_mp 8.82 A
V_oc
0.7379 V | I_sc 9.345 A
Efficiency
23.2%
Temp Coeff
−0.29 %/°C
Cost/cell
$0.8727
Panel Power
720 W (66S × 2P cells)
Panel Area
3.11 m²
ARRAY CONFIGURATION
Orientation
Landscape
Layout
2 cols × 2 rows
Max Fit
4 panels (roof limited)
String Config
4S × 1P
String Voltage
163.2 V DC
Array Current
17.67 A
DC Capacity
2.88 kW
Area Used
12.44 m² (100%)
Battery
Generac PWRcell M6
SCENARIO COMPARISON
PV ONLY
Panels
4 (2.88 kW DC)
Battery
None
CAPEX Gross
$506.88
Net (after 30% ITC)
$354.82
Annual Savings
$2,155 / yr
Grid Import
13,643.7 kWh/yr
Grid Export
77.9 kWh/yr
Annual Bill
$6,868.94
Payback
1 year
10-yr NPV
$17,791
PV + BATTERY
Panels
4 (2.88 kW DC)
Battery
Generac PWRcell M6
CAPEX Gross
$13,156.88
Net (after 30% ITC)
$9,209.82
Annual Savings
$2,193 / yr
Grid Import
13,559.4 kWh/yr
Grid Export
0.0 kWh/yr
Annual Bill
$6,831.46
Payback
4 years
10-yr NPV
$9,250
10-YEAR CASH FLOW BREAKDOWN
Yr
Traditional $
PV-Only $
PV Savings $
PV Cumul. $
PV+Bat $
Bat Savings $
Bat Cumul. $
1
$9,039
$6,888
$2,150
$2,150
$6,854
$2,184
$2,184
2
$9,581
$7,304
$2,277
$4,428
$7,267
$2,314
$4,498
3
$10,156
$7,744
$2,411
$6,839
$7,706
$2,450
$6,948
4
$10,765
$8,212
$2,553
$9,392
$8,171
$2,594
$9,543
5
$11,411
$8,709
$2,702
$12,094
$8,664
$2,747
$12,289
6
$12,096
$9,235
$2,860
$14,955
$9,188
$2,907
$15,196
7
$12,821
$9,794
$3,027
$17,982
$9,744
$3,077
$18,274
8
$13,591
$10,388
$3,203
$21,185
$10,334
$3,256
$21,530
9
$14,406
$11,017
$3,389
$24,573
$10,960
$3,446
$24,976
10
$15,270
$13,685
$1,585
$26,159
$13,625
$1,646
$26,621
Assumptions: 30% Federal ITC · 6% annual utility inflation · 7% discount rate · 0.5%/yr panel degradation · Year-10 inverter replacement reserve
ECE 285 · UCSD · Residential Solar Optimization | Slide 4 of 4

## Slide 10
Residential Energy
System Optimizer
Python · MILP · Solar + Storage Sizing for San Diego Homes
A comprehensive Python framework that automates the sizing, physical layout, and dispatch scheduling of residential solar and battery storage systems. It uses a joint Mixed-Integer Linear Program (MILP) to optimize capital sizing and a full year of hourly energy dispatch simultaneously — avoiding the errors of simulate-after-sizing heuristics.
Dynamic Data Ingestion
Roof Geometry ('Tetris')
Joint MILP Optimization
10-Year Financial Engine
43,803
MILP Variables
8,760
Hours Optimized
2 Runs
PV-Only · PV+Battery
ECE 285 · UCSD · Smartgrids
ECE 285 · UCSD · Residential Solar Optimization | Slide 1 of 4

## Slide 11
02
System Inputs
What the optimizer needs to know — and why each input matters
USER-PROVIDED INPUTS
location
GPS coordinates → drives irradiance fetch & load downscaling
budget_usd
Max total spend → caps CAPEX in the MILP objective
roof_width_m,
roof_length_m
Physical roof dims → limits how many panels physically fit
tariff_plan
Chooses SDG&E rate schedule → sets hourly electricity prices
annual_consumption_kwh
Yearly energy use → anchors the 8760-hr load profile
num_occupants
Scales EIA load data to match household size
EXTERNAL DATA SOURCES
Open-Meteo Irradiance API
GHI(t)
Global Horizontal Irradiance per hour → PV generation input
G_ref
Reference irradiance (STC) → normalizes panel output
T_ambient(t)
Ambient temp per hour → applies panel temp coefficient loss
EIA Residential Load Database
Load(t)
Hourly demand profile → enforced as power balance constraint
load_scale
Occupant + geographic factor → adjusts kWh to match household
annual_kwh_eia
5-yr averaged baseline → rescaled to user's stated consumption
variability_k
9-factor weighting (coastal, inland, HVAC…) → realism of profile
HARDWARE CATALOGS
Solar Panel Catalog (8 models)
efficiency_%
Cell-to-area conversion → determines panels needed per m²
cost_per_wp
$/Watt-peak → optimizer selects best efficiency-to-cost ratio
temp_coeff
Power loss per °C → applied to hourly generation model
V_mp, I_mp
MPPT operating point → sizes string for 400V inverter target
panel_area_m²
Physical footprint → Tetris geometry checks roof fit
Battery Storage Catalog (5 models)
capacity_kwh
Usable energy storage → sized by MILP to minimize grid cost
RTE_%
Round-trip efficiency → accounts for charge/discharge losses
P_charge_max,
P_discharge_max
Power limits → constrain hourly charge & discharge rate
cost_usd
Unit price → added to CAPEX if battery scenario selected
ECE 285 · UCSD · Residential Solar Optimization | Slide 2 of 4

## Slide 12
03
Processing Pipeline
Roof Geometry · MILP Formulation · Constraints · HiGHS Solver
STEP 1 — ROOF GEOMETRY
Orientation Search
Tests portrait & landscape for every panel model. Picks the orientation maximizing roof_area_utilization (%) — the ratio of panel footprint to available roof_area_m².
Panel Fit (Tetris Approach)
Divides roof_width_m and roof_length_m by the panel's physical dims to find max panels per row and max rows. Integer math — no partial panels allowed.
String Wiring
Iterates over (panels_in_series × parallel_strings) combinations. Selects config minimizing |string_voltage − inverter_target_v|, respecting total panel count.
Array Output
Computes total_dc_capacity_kw = N × P_panel_w. This upper-bounds PV(t) in the MILP, ensuring the optimizer never exceeds physical generation.
STEP 2 — MILP FORMULATION
Decision Variables
N_panels (integer) · BatCap_kwh (continuous)
Import(t) · Export(t) · Charge(t) · Discharge(t) · SOC(t) — one value per hour t
Objective Function
Minimize:
(Net_CAPEX × annuity_factor)
+ Σ tariff(t) × Import(t)
− Σ export_credit(t) × Export(t)
Power Balance (enforced every hour)
Load(t) = PV(t) + Discharge(t) + Import(t)
− Charge(t) − Export(t)
Battery Health
SOC_floor ≤ SOC(t) ≤ SOC_max
Charge(t) ≤ P_charge_max
SOC(t+1) = SOC(t) + Charge(t)·η − Discharge(t)/η
Capital Bounds
N_panels ≤ max_panels_fitting_roof
Total_CAPEX ≤ budget_usd
30% ITC applied → Net_CAPEX = Gross × 0.70
STEP 3 — SOLVER OUTPUT
Dual Run Design
Run 1 solves PV-Only. Run 2 solves PV + Battery. Same model, same constraints — the battery capacity variable is simply unlocked in Run 2. Direct A/B comparison with identical boundary conditions.
PV Generation Model
PV(t) = N_panels × P_panel_w × (GHI(t) / G_ref) × PR
Performance ratio PR accounts for wiring, inverter, and soiling losses. Degradation applied per year.
Dispatch Simulation
Post-solve: replays the optimal N_panels and BatCap through hourly dispatch rules to compute exact grid_import_kwh, grid_export_kwh, and electricity bills for each scenario.
Solver Engine
scipy.optimize.milp → HiGHS backend.
Sparse constraint matrix (csc_matrix) keeps memory low despite the large horizon. Both runs solve to Optimal status.
ECE 285 · UCSD · Residential Solar Optimization | Slide 3 of 4

## Slide 13
04
Results & Outputs
What the system returns — and what each output means for the homeowner
HARDWARE CONFIGURATION
selected_panel
Chosen model (best efficiency/cost) → confirms what gets installed on the roof
N_panels
Optimal integer count → determined by MILP to minimize cost within roof & budget limits
orientation
Portrait or landscape → layout that maximizes roof area utilization
panels_in_series,
parallel_strings
String wiring config → meets inverter voltage target; affects system safety & warranty
total_dc_capacity_kw
N × P_panel_w / 1000 → max power the array can produce at STC; used to size inverter
roof_utilization_%
How much of the roof is covered → tells homeowner if more panels could fit with a larger roof
BATTERY CONFIGURATION
battery_required
True/False → whether storage is economically justified given tariff & load profile
selected_battery
Chosen model → best usable capacity per dollar from catalog
units_required
Number of battery units → scales capacity to meet optimal BatCap_kwh from MILP
total_capacity_kwh
Usable stored energy → covers peak-rate hours, reducing grid_import cost
P_max_charge_kw,
P_max_discharge_kw
Power limits → determines how fast battery can shift energy; inverter sizing input
round_trip_eff_%
Energy retained per cycle → directly reduces net savings if low; factored into every SOC update
FINANCIAL OUTPUT
gross_capex_usd
Panel + battery + install costs → what homeowner pays before incentives
net_capex_usd
After 30% Federal ITC → real out-of-pocket cost to compare scenarios
annual_savings_usd
Traditional bill minus solar bill → yearly dollar benefit; grows with inflation_rate
simple_payback_yrs
net_capex / annual_savings → how many years until the system pays for itself
npv_usd
Net Present Value over 10 years at discount_rate → true economic value of the investment
ten_year_breakdown[]
Year-by-year cash flow table → shows cumulative savings and bill comparison over time
FINANCIAL MODEL ASSUMPTIONS
inflation_rate
Annual utility price growth
discount_rate
Time-value of savings
degradation_rate
Annual panel output loss
itc_rate
Federal solar tax credit
inverter_reserve_yr
Year-10 replacement cost
ECE 285 · UCSD · Residential Solar Optimization | Slide 4 of 4